## Slide 1: Appliances for domestic biogas plants
Biogas compact course
PPRE- Oldenburg University
April 26 28, 2011

## Slide 3: Presentation Planning
Household gas use
Combustion process
Stoves design criteria
Lamps
Importance of appliances
Refer to the reader

## Slide 4: Household gas use
The average household biodigester is not suitable to run a electricity generator
Biogas cannot be bottled
It is an excellent energy source for cooking and lighting which accounts for more than 95% of rural domestic energy use

## Slide 5: “Bottling biogas”

## Slide 6: Advantages of biogas for cooking
CONVENIENCE
  time-saving; wood collection and cleaning: Vietnam 1,5 to Nepal 6 h/d
  cooking faster; flame can be regulated;
  cooking can be done in up-right position;
  cooking can be easily done inside the house;
FINANCE
  Saves money on energy sources
HEALTH
  fine particles and CO: smoke world death-cause nr. 3 AIDS Malaria; 1.6 mln death per year
  safer, less chance for accidences like with open fire

## Slide 7: Combustion process during cooking

## Slide 8: Combustion process during cooking
Primary air intake ~ 90%, secondary air 10%
5.7 volume air is required for 1 volume biogas for complete combustion
Mix too rich: incomplete combustion, CO emission, less efficiency
Mix too lean: too much air cools the flame, less efficiency
Combustion speed 40cm/sec

## Slide 9: Stove design

## Slide 10: Stove design
Burner design criteria:
Starting values:
QR [kcal/h] = prescribed heat requirement
VF [m3/h] = fuel flow rate
H [m W.C.] = prescribed gas pressure
Geometrical data:
do [mm] = 2.1 * √(VF/√h) (jet diameter)
d [mm] = 6 * do (diameter mixing pipe)
l [mm] = 7 * d (length of mixing)

## Slide 11: Stove design considerations
Efficiency > 55%
User comfort (position of the tap, gas flow regulation capacity of the tap, primary air intake regulation)
Stability of the frame, distance burner – frame support
Stability of the cooking vessel on the pan supports
Distance bottom cooking vessel – flame ports burner, 25 – 30 mm
CO emissions
Manufacturing simplicity, locally made preferably by various rural workshops
Cost

## Slide 13: Stove test results
Name | Burner | Pan height | CO PPM | Flue temp | Time to Boil (mins)
Test 1 | standard | 32 mm | 251 | 84 | 4.9
Test 2 | lotus | 32 mm | 203 | 87 | 5.0
Test 3 | lotus | 39 mm | 32 | 89 | 5.2
Test 4 | standard | 39 mm | 286 | 82 | 4.8

## Slide 15: Stove testing under basic lab conditions
Gas and temperature sensor
John
Stove
Meter
Flue
Filter

## Slide 16: More stove tests

## Slide 17: And some stunning results …

## Slide 19: And a shroud is not solving the problems …

## Slide 20: Biogas stove standards
..\..\2010 Quality Management\03 QS Appliances\QS Appliances Text files\Biogas Stove Part 1.doc

## Slide 22: Quality Quotes
Good is not good where better is expected." -- Thomas Fuller
The bitterness of poor quality lingers long after the sweetness of low price.
If you think training is expensive...consider ignorance. – Anonymous

## Slide 24: Dome Gas Pipe

## Slide 25: Mixer

## Slide 26: Gas tap

## Slide 27: Gas Tap

## Slide 28: Water Drain

## Slide 29: Biogas Stove

## Slide 30: Dome Template

## Slide 31: Biogas Injerra Stove

## Slide 32: Biogas rice cooker (China)

## Slide 33: WHO: 1.6 mln people die each year of fumes

## Slide 34: Improved kitchen

## Slide 35: Fuel matrix
Fuel | Unit | Heat value kCal/Unit | Stove | Efficiency | Amount of biogas eq
Biogas | m3 | 5,200 | Gas stove | 60 | 1
Straw | Kg | 3,300 | Tripod stove | 11 | 8.60
Wood | Kg | 3,800 | Tripod stove | 16 | 5.00
Charcoal | Kg | 6,900 | Oven | 28 | 1.62
Kerosene | Litre | 9,100 | Oil stove | 45 | 0.76
LPG | m3 | 25,000* | LPG stove | 60 | 0.20
Electricity | kWh | 860 | Electric cooker | 70 | 5.18

## Slide 37: Current Developments
In cooperation with the African and Lao biogas programmes the NBP in Cambodia has made a R&D contract with a mechanical development agency with the following objectives
Improvement of the present design biogas stove manufactured in Cambodia;
Development of a complete package of documentation and special tools required for the manufacturing of the improved stove, and;
Training package development for vocational trainers and workshop technicians on the manufacturing of the stoves.

## Slide 38: Lotus Biogas Stove

## Slide 39: Applying biogas for light

## Slide 40: Benefits of applying biogas: light
Capacity comparable with 60-75 W incandescent lamp
CONVENIENCE
Backup to unreliable electricity grid
Replacement for –costly- batteries, candles, kerosene, etc.
Gives light where is used to be dark
Low gas use, 80 – 100 liters/hour
SAFER
Reduces the risk of fire in the house when well positioned and care is take when the mantle needs to be replaced
HOWEVER
Poor efficiency of only 3% (Kerosene lamp 6%)
Very high temperature is needed to glow 1,000-1,500 C
Frequent change of mantle

## Slide 41: Biogas lamps
Will fulfill a demand for good quality light
Difficult to be made by small scale workshops
Cheap large scale production in China and India
Need a good service infrastructure (regular need for spare-parts)
Need quality user training for operation and maintenance

## Slide 43: Lamp design China
Nozzle and injector
hanger
connecting piece
inlet for primary air
injector
nut
washer
upper cover
clay head
air vent
clip pin
reflector
glass cover

## Slide 44: Lamp design India

## Slide 47: THANK YOU VERY MUCH!